## Slide 1: October 19, 2018 Draft Toxicity Provisions
BACWA Permits Committee Meeting
November 13, 2018

## Slide 2: What’s going to change?
NEW! Chronic toxicity limits
NEW! Tests analyzed by Test of Significant Toxicity (TST)
NEW! Implementation plan that supersedes Basin Plan
No change to EPA WET Test Methods

## Slide 3: What’s different about the TST?
SAME toxicity test method, DIFFERENT statistical evaluation
TST is performed only at Instream Waste Concentration (IWC), not using dose-response curve
TST give a “pass” or “fail”, rather than a measure of toxicity like TUc
Agencies can input historic toxicity data at IWC into TST calculator to see if they would have passed

## Slide 4: How bad is the TST?
Different opinions, but two major concerns:
Increase rate of false determinations of toxicity compared to EC25, punishes high variability
  Some species (Ceriodaphnia dubia) have inherently high variability. BACWA is partially funding a White Paper to look more closely at this issue.
No recourse for anomalous dose-response curves

## Slide 5: The TST punishes variability
Chart: 
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
low variability | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.5 | 8 | 16 | 25 | 16 | 8 | 3.5 | 0 | 0 | 0 | 0 | 0 | 0
medium variability | 0 | 0 | 0 | 0 | 0 | 1.5 | 3.5 | 7 | 11 | 18 | 20 | 18 | 11 | 7 | 3.5 | 1.5 | 0 | 0 | 0 | 0
high variability | 0 | 0 | 0.5 | 1 | 2 | 3.5 | 5 | 7 | 9 | 11 | 12 | 11 | 9 | 7 | 5 | 3.5 | 2 | 1 | 0.5 | 0
limit

## Slide 6: TST only looks at the IWC
Chart: Anomalous dose-response curve
| 0 | 10 | 20 | 40 | 60 | 80 | 100
% effect | 0 | 5 | 10 | 30 | 15 | 4 | 12

## Slide 7: TST Litigation
BACWA joined SCAP and CVCWA in ongoing lawsuit alleging EPA is improperly requiring use of unpromulgated method
EPA objects on basis of statute of limitations

## Slide 8: Current Toxicity ProvisionsStatus
New Draft Toxicity Provisions Released – October 19, 2018
Now proposed as a component of the State’s Inland Surface Waters, Enclosed Bays, and Estuaries Plan
  It is to be “Provisions” in the SIP, not a “Policy”
  Will not require amending the Basin Plan
They did make some changes in response to comments!

## Slide 9: What will go in your permit?

## Slide 10: Minimum Monitoring Frequencies
Routine testing
For POTWs ≥ 5 MGD – Chronic Testing Monthly
For POTWs < 5 MGD – Chronic Testing Quarterly
Most Sensitive Species Screens
  Three toxicity tests conducted concurrently using three different species.
  Repeated four times.
    Quarterly for one year for continuous dischargers
    Evenly spaced through out a year for non-continuous dischargers
  At least once in ten years, “unless the discharger is participating in a regional monitoring program”

## Slide 11: Reasonable Potential - Who Will Get Numeric Limits?
For POTWs ≥ 5 MGD – You Have Assumed RP
For POTWs < 5 MGD – If any single test exhibits a 10% effect or greater, you will have RP

## Slide 12: Who is <5 mgd?
Crockett
St. Helena
Yountville
Calistoga
Rodeo
SMCSD
Treasure Island
American Canyon
Las Gallinas
Millbrae
Sonoma
Mt View
SFO Airport SASM Pacifica
Pinole
Benicia

## Slide 13: What will the Limits look like? MDEL
No chronic toxicity test shall result in a “fail” at the IWC for the sub-lethal endpoint measured in the test AND a Percent Effect for the survival endpoint greater than or equal to 50%
Or if no survival endpoint can be measured, then:
No chronic toxicity test shall result in a “fail” at the IWC for the sub-lethal endpoint measured in the test and a Percent Effect for the sublethal endpoint greater than or equal to 50%

## Slide 14: What Will The Limits Look Like? MMEL
Routine Monitoring Test | Compliance Test 1 | Compliance Test 2 | MME Violation?
Pass | NA | NA | No
Fail | Pass | Pass | No
Fail | Pass | Fail | Yes
Fail | Fail | NA | Yes

## Slide 15: Can we really do three tests in one calendar month?
The PERMITTING AUTHORITY shall specify the day of the month that corresponds to the start of a CALENDAR MONTH...
If an acute or chronic toxicity ROUTINE MONITORING test results in a “fail” at the IWC, then NON-STORM WATER NPDES DISCHARGERS shall conduct a maximum of two MMEL COMPLIANCE TESTS. The MMEL COMPLIANCE TESTS shall be initiated within the same CALENDAR MONTH that the first ROUTINE MONITORING test was initiated that resulted in the “fail” at the IWC.

## Slide 16: Reduced Compliance Monitoring Frequency
Temporary reduction in routine monitoring allowed during a TRE
    Twice per year (every 6 months)
Reduction in Routine Monitoring if:
    MDEL and MMEL has not been exceeded for five years.
    Toxicity provisions in the NPDES Permit have been followed.

## Slide 17: Areas for Regional Water Board discretion
Acute toxicity RPA
IWC
Reduced compliance monitoring during TRE/TIE

## Slide 18: Compliance Challenge!
Because toxicity limits are NEW, and because the TST has a higher rate of false determinations of toxicity, many agencies will violate their toxicity limits
This threatens clean compliance records
Agencies producing recycled water don’t want their effluent labeled as “toxic”

## Slide 19: Next steps
Public workshop October 31
State Water Board hearing November 28
Written comments due December 7
Adoption April 2019
Discussion of BACWA Comment Strategy at November Board Meeting – What can we change at this point?

## Slide 20: Potential comments
Big Picture:
  NO TST!
  NO numeric limits!
  We should be allowed to use dose response curves to invalidate tests
  No MDEL
Implementation details
  10% threshold for RPA is too low
  Historic data should be allowable for monitoring offramp
  Limit Regional Water Board discretion
  Increase time for MMEL testing