## Slide 1: Chlorine Residual Basin Plan Amendment Project Update
BACWA Executive Board Meeting
04/20/2018

## Slide 2: Cl2 Compliance Issue
Basin Plan 0.0 mg/L chlorine residual effluent limit
Instantaneous maximum limit
Continuous monitoring required
Transient/false positive readings occur
Mandatory minimum penalty (MMP) for each excursion
  Any measured concentration
  Any measured duration
  MMP minimum $3,000/excursion
  No RWB enforcement discretion

## Slide 3: Interim Compliance Approach
BACWA 2002/2003 Cl2 compliance investigations
RWB/BACWA 2004 letter agreement
Report 24 every hour on the hour readings daily (MMPs)
Narrative off hour excursion reporting
  For RWB discretionary enforcement (infrequent)
  Not in every permit (footnotes)

## Slide 4: CIWQS Excursion Info
CIWQS queries 01/01/2010 – 12/31/2017 (8 years)
All SF Bay NPDES permits with MMPs (incl. potable)
  Manually inspect MMPs for POTW Cl2 concentrations
  Manually inspect SMR cover letters for event durations
14 POTWs reported Cl2 excursions
32 total excursions (1 to 6 per year – no trend)
0.001% Cl2 excursion rate

## Slide 5: Excursion Results
Maximum of each event reported to CIWQS (vs range)
Repeat excursions infrequent
  2 POTWs w/6 excursions
  3 POTWs w/3; 2 w/2; 7 w/1
Average of all reported excursion events
  Cl2 concentration = 1.66 mg/L
  Event duration = 29.4 minutes
Cumulative frequency distribution (graphs)
  50th %ile concentration < 2 mg/L
  50th %ile duration < 30 minutes

## Slide 6
Chart: SF Bay POTWs 2010 - 2017 Chlorine Residual Excursion Concentrations – Cumulative Frequency
| 1 | 10.82 | 0.13 | 1.61 | 1.2 | 0.1 | 0.47 | 0.9 | 6.45 | 1.25 | 5.3 | 0.27 | 0.2 | 3.7 | 2.5 | 0.2 | 0.3 | 1.8 | 0.08 | 0.41 | 1.4 | 1.53 | 0.82 | 1.4 | 0.24 | 0.4 | 0.45 | 2.2999999999999998 | 2.79 | 1.7 | 0.75 | 0.63
CDF | 0.38374 | 0.99998 | 0.24643 | 0.49117 | 0.4184 | 0.2422 | 0.29691 | 0.36674 | 0.98415 | 0.42718 | 0.94871 | 0.26664 | 0.25643 | 0.81991 | 0.64689 | 0.25643 | 0.27108 | 0.52514 | 0.23941 | 0.28766 | 0.45371 | 0.47687 | 0.35332 | 0.45371 | 0.26224 | 0.28614 | 0.29381 | 0.61304 | 0.69391 | 0.50727 | 0.34172 | 0.32219

## Slide 7
Chart: SF Bay POTWs 2010 - 2017 Chlorine Residual Excursion Durations – Cumulative Frequency
| 87 | 0.7 | 3 | 15 | 19 | 23 | 90 | 29 | 10 | 12 | 11 | 9 | 60 | 15 | 27 | 1 | 6 | 5 | 9 | 75 | 83 | 71 | 15
 | 0.96982 | 0.17495 | 0.19495 | 0.31965 | 0.36757 | 0.41765 | 0.97592 | 0.49508 | 0.26381 | 0.28554 | 0.27457 | 0.25327 | 0.84089 | 0.31965 | 0.4691 | 0.17748 | 0.22302 | 0.21342 | 0.25327 | 0.9315 | 0.95975 | 0.91256 | 0.31965

## Slide 8: Cl2 Effluent Limit Approach
Delete 0.0 mg/L limit in Basin Plan Table 4-2
Add EPA 1985 Ambient Water Quality Criteria to BP
  Saltwater Cl2 WQC: 13 ug/L as 1-hour average
  Freshwater Cl2 WQC: 19 ug/L as 1-hour average
Water quality based effluent limits (WQBEL)
  Deepwater POTWs: use actual dilution (consider updates)
  Shallow-water POTWs: derive new reporting limit (RL)
  Limited RL precedents for wastewater on-line monitoring

## Slide 9: Compliance Determination
New 1-hour average limit vs old instantaneous max
  Use continuous analyzer monitoring data
  How many truly discrete analyzer readings per hour?
  Retain single on the hour instantaneous reporting?
  Use average of 12 5-minute results per hour?
Other potential add-on compliance criteria
  No individual excursion shall exceed X minutes
  No individual excursion shall exceed Y mg/L
  Total excursions shall not exceed Z min/month

## Slide 10: Bisulfite Overdosing
Over-dosing required for consistent compliance
Bay-wide about 3 MG of sodium bisulfite used annually
Bay-wide annual (2017) bisulfite costs about $3.5 M
Amount of over-dosing unknown
Estimate OD reduction (benefits) for BPA justification
Preparing BACWA member survey
  Bisulfate usage
  Over-dosing protocols
  Potential reductions after BPA

## Slide 11: Contact Information
Tom Hall, Ph.D.
EOA, Inc.
twhall@eoainc.com