## Slide 1
Pretreatment “Master Class” Training
BACWA/EBMUD Pretreatment Training
March 11, 2019
Greg V. Arthur - (510) 967-8411 - gva@gvaarthur.com
2015-2019 Creekside Community Church
2013-2015 Former Senior Project Engineer
EEC Environmental
1983-2013 Now Long Since Retired Environmental Engineer
Region 9, Clean Water Act Compliance Office
U.S. Environmental Protection Agency

## Slide 2
Industrial User Inspections
BACWA/EBMUD Pretreatment Training
March 11, 2019
Greg V. Arthur - (510) 967-8411 - gva@gvarthur.com

## Slide 3
Industrial User Inspections
Key is to find the sources of variability in discharge quality
Fed Requirements
Inspection Types
Conducting the
Inspections
Documentation
Inspection Reports
Permit Fact Sheets
Finding Sources of
Variability
Representativeness
Bypass / Dilution
batch industrial wastewater treatment unit for oil and toxic shipyard process waters
C

## Slide 4
Industrial User Inspections
Key is to find the sources of variability in discharge quality
Fed Requirements
40 CFR 403.8(f)(2)(v)
POTWs must
determine compliance
independent of the
information provided
by the discharger
sampling
inspection
verification
portable pump with long extension hoses in an electroplating shop
D

## Slide 5
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Inspections Types
Unannounced
Announced
Sampling
Non-Sampling
Walk-Through
Comprehensive
Civil Enforcement
Criminal Investigation
batch industrial wastewater treatment unit for spent solutions and IX regenerant
C

## Slide 6
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 1 - Entry
always present
credentials
always explain the
inspection purpose
always explain use
of confidential info
always explain
use of photographs
always stay in
public in plain sight
continuous pH and ORP metering for treatment found not in service
“I am Greg Arthur, an inspector with US EPA Region 9 in the Clean Water Act Compliance Office. I am conducting routine inspections of certain industrial users in order to verify the basis of the municipal permit and to make findings toward the determination of compliance. This is a routine inspection and not one in which you were singled out. I’m required to always present my credentials upon setting foot on facility property and so here are my credentials. My intention is to walk-through the facility, verify the configuration of wastewater handling, and set-up a 24-hour composite sampler at the permitted sample point. I would like to take pictures during this inspection strictly of valves and pipes and things like that, that depict wastewater generation sources, delivery methods, treatment, and disposal, and I will ask you for permission before each picture. If you believe that anything I ask is confidential, please notify me of this, as it is not my intention to handle any confidential information. However, effluent data, and flow or production rates needed to determine compliance are expressly not confidential. Do you have any questions of me before we start?”

## Slide 7
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 1 - Entry
write all this in the
field notebook
prepare but don’t
overprepare - know:
1 - the permit
2 - permit fact sheet
3 - IU submissions
4 - current permitting
compliance issues
opening conference
announced inspection
Unannounced inspections to collect samples, for example, should simply involve the presentation of credentials.
Announced inspections would involve an opening conference, followed by the escorted inspection of the facility. The opening conference should also lay out which samples are going to be collected during the inspection – splits, dupes, blanks. In my opinion, for routine POTW sampling, it must be assumed the results could be used in an enforcement action. Therefore, at each facility per day, there should be one sample duplicate, one field blank, and an offer to split a sample. The rule of thumb at EPA was one dupe and one blank for every ten samples taken in a day.
I always said and did the same thing so that if I ever had to testify I could say, “I know I presented my credentials and announced my purpose for the inspection because I always present my credentials and announce my purpose for the inspection”.

## Slide 8
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 2 - Process
First follow the indus-
trial processing steps
(raw materials in to
final products out).
open drums, portable pump and hosing, floor staining – general uncontrolled mess
“If you could lead me from the start of the process to the end, as if we are raw materials. Along the way I will note where wastewaters and wastes are generated, and how they are delivered to their points of disposal. Only after following the process from raw materials in to finished products out, would I then like to double back and see the points of delivery, treatment, and disposal. This way I am able to first understand the sources in order to better grasp the layout and configuration of the wastewater handling on-site.”

## Slide 9
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 2 - Along the way
identify all
wastestreams
determine
controls for each
determine all
methods of delivery
verify the
pollutants present
verify process
and start-up dates
open drums, portable pump and hosing, floor staining – general uncontrolled mess
DD

## Slide 10
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 3 – Control
Inspect all treatment
units and methods of
pollution control and
wastewater handling
practices
industrial wastewater treatment unit with final storage and equalization

## Slide 11
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 3 – At Each Point
identify all
incoming sources
identify reaction
end-point controls
determine methods
of internal delivery
verify reagents and
pollutants present
identify all outgoing
wastestreams
industrial wastewater treatment unit with final storage and equalization
C

## Slide 12
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 4 - Disposal
Verify sample points,
sampling frequencies,
and pollutants
sampled against
pollutants present
sewer connection discharge point with multiple wastewater inlets

## Slide 13
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 4 - Disposal
determine if sampling
accounts for all flows
verify sample day
representativeness
verify representativ-
ness over time
determine
methods of disposal
verify sampling covers
pollutants present
sewer connection discharge point with multiple wastewater inlets
D

## Slide 14
industrial wastewater treatment unit with continuous reaction end-point metering
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 5 - Schematic
Get enough detail to
draw a wastewater
control schematic

## Slide 15
Wastewater
Control
Schematic
Level of Detail
sources
and schedules
methods of
delivery
methods of
control
unit process
monitoring
methods of
disposal

## Slide 16
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Step 5 - Schematic
Completing a waste
water schematic on-
site gives the best
understanding of the
facility by far!
industrial wastewater treatment unit with continuous reaction end-point metering
Metering for
chrome reduction
metals precipitation
cyanide destruction
C

## Slide 17
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Field Notes
and Documentation
Should Stand Alone
all findings clearly
described and dated
attribution of all
sources of information
all statements made
recorded and dated
all conclusions clearly
marked as such
multiple discharges from continuous and batch treatment units to single outlet

## Slide 18
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Field Notes
and Documentation
Should Stand Alone
questions to yourself
for further investigation
opening conference
statements recorded
close-out interview
statements recorded
collected documents
and photos listed
multiple discharges from continuous and batch treatment units to single outlet

## Slide 19
Field Notebook
Valley Plating 2009

## Slide 20
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Field Notes
and Documentation
It’s Your Testimony
so write it down even
if you already know it
multiple discharges from continuous and batch treatment units to single outlet

## Slide 21
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Inspection Reports
and Permit Fact Sheets
Administrative Record
all findings clearly
described and dated
attribution of all
sources of information
citation of pertinent
ordinances and rules
itemize requirements
and recommendations
multiple discharges from continuous and batch treatment units to single outlet

## Slide 22
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Inspection Reports
and Permit Fact Sheets
Administrative Record
use “shall” for all
requirements
use “should”, or better
yet, “should consider”
for recommendations
use to document
photos (used/unused)
include a wastewater
control schematic
multiple discharges from continuous and batch treatment units to single outlet

## Slide 23
Industrial User Inspections
Key is to find the sources of the variability in discharge quality
Inspection Reports
and Permit Fact Sheets
Administrative Record
keep administrative
information up to date
(1) phone numbers
(2) e-mail addresses
(3) names / job titles
(4) permit numbers
(5) permit dates
(6) sewer service area
and NPDES permit
(7) addresses
multiple discharges from continuous and batch treatment units to single outlet
D

## Slide 24
Inspection Report
Cover Letter

## Slide 25
Inspection Report
Title Page

## Slide 26
Inspection Report
Facility Description

## Slide 27
Inspection Report
Facility Description

## Slide 28
Inspection Report
Facility Description

## Slide 29
Inspection Report
Wastewater
Control Schematic

## Slide 30
Inspection Report
Facility Photo
Documentation

## Slide 31
Inspection Report
Permit Verification

## Slide 32
Inspection Report
Permit Verification

## Slide 33
Inspection Report
Permit Verification

## Slide 34
Inspection Report
Permit Verification

## Slide 35
Inspection Report
Compliance
Determinations

## Slide 36
Inspection Report
Compliance
Determinations

## Slide 37
Inspection Report
Compliance
Determinations

## Slide 38
Finding Sources of Variability
Key is to find the sources of the variability in discharge quality
Conducting Inspections
Ultimately industrial
users meet effluent
limits by controlling
the variabilities
inherent in the design
and operations, that
effect wastewater
quality.
continuous pH and ORP metering for treatment found not in service

## Slide 39
pH and ORP probes
evidently not used recently
continuous pH and ORP metering for treatment found not in service
Finding Sources of Variability
Key is to find the sources of the variability in discharge quality
Conducting Inspections
So … focus field work
on identifying and
quantifying sources
and controls of
variabilities from
operations
treatment
discharge
D

## Slide 40
Finding Sources of Variability
Key is to find the sources of the variability in discharge quality
Operational
Sources of Variability
Variabilities in waste-
water generation are
the result of the way
the industry operates
and in how the wastes
are then collected,
delivered, treated, and
conveyed for disposal.
bosses - operators - contractors - grunts
and a couple of plating shop dudes

## Slide 41
bosses - operators - contractors - grunts
and a couple of plating shop dudes
Finding Sources of Variability
Examples of variabilities related to operations
Variability in Flow
seasonal
weekends
swing shift
timer
scheduled overhaul
CIP
D

## Slide 42
Finding Sources of Variability
Examples of variabilities related to operations
Variability in
Pollutant Loadings
spents
circulation bleeds
regenerant / reject
concentrates
CIP tank flush
sump drainage
treatment unit
tailwaters
floor drains - wet floors
D

## Slide 43
Finding Sources of Variability
Examples of variabilities related to operations
Wastewater Segregation
by Strength
high-strength
spents
drag-out spents
IX regenerant
low-strength
overflow rinses
washdown
hydrotest
uncontaminated
RO/IX brines
domestic sources
hardpiping of spents by type to segre-gated batch treatment + clear labeling
C

## Slide 44
Finding Sources of Variability
Examples of variabilities related to operations
Wastewater Segregation
by Treatability
cyanide-bearing
acids
alkalines
oily emulsions
brines
solids and slurries
insoluble organics
soluble organics
volatile organics
separate tanks for different types of batch treatment steps
C

## Slide 45
on-demand low-overflow rinsing
Finding Sources of Variability
Examples of variabilities related to operations
Process Water
Consumption Practices
on-demand
countercurrent
dilution
DI make-up
IX in-tank circulation
CIP schedules
C

## Slide 46
Finding Sources of Variability
Key is to find the sources of the variability in discharge quality
Treatment-Related
Sources of Variability
Treatment reduces
variability in effluent
quality (1) by reducing
mean concentrations
and (2) because effec-
tive treatment requires
control of the influent
quality, delivery, and
treatment processes.
oily wastewater treatment unit for oily bilge and ships wastewater

## Slide 47
Finding Sources of Variability
Examples of variabilities related to treatment
separate treatment
by strength
reaction end-points
reaction interference
settling / filtration
design capacity
surges
short-circuiting
clogging
solids handling
variability controls
equalization
metering
oily wastewater treatment unit for oily bilge and ships wastewater
C

## Slide 48
segregated wastewaters collected for off-site disposal
Finding Sources of Variability
Key is to find the sources of the variability in discharge quality
Discharge-Related
Sources of Variability
The methods of dis-
charge and disposal
can significantly reduce
the variabilities in the
effluent quality.

## Slide 49
segregated wastewaters collected for off-site disposal
Finding Sources of Variability
Examples of variabilities related to the method of discharge
combined discharge
batch discharge
metered discharge
final equalization
test prior to discharge
off-site disposal
C

## Slide 50
Industrial User Inspections
BACWA/EBMUD Pretreatment Training
March 11, 2019
Questions or Comments
Greg V. Arthur - (510) 967-8411 - gva@gvarthur.com